## Slide 1: An Evaluation of Apollo Powered Descent Guidance
Lloyd David Strohl III

## Slide 2: Statement of Purpose

## Slide 3: Powered Descent Guidance
Powered descent phase required for any mission in low or no atmosphere
Apollo Powered Descent Guidance (APDG) flown in vacuum only
Simple implementation makes APDG an easy testbed for Adaptive Powered Descent Initiation strategy

## Slide 4: Adaptive Powered Descent Initiation
Most powered descent strategies rely upon time-to-go estimate
Predetermined ignition point is open-loop. Closed-loop strategy might provide better performance and safety
Adaptive PDI helps improve safety and performance automatically

## Slide 5: Manned Mars Mission
Manned Mars missions are the focus of current efforts in aerospace, including NASA, SpaceX, and others
Manned Mars missions have high payload mass and large propellant inefficiency penalty
Safety criticality for landing
Thin but significant atmosphere
Vehicle studied is CobraMRV (Cerimele et al)

## Slide 6: Problem Statement
Powered Descent and Landing for Manned Mars Mission
  Powered descent takes over after successful de-orbiting and aerobraking maneuver, when vehicle is controllable in glide near landing site
Assumptions for formulation of guidance law
  Atmospheric forces neglected
  Rotation of planetary body accounted for by terminal conditions and guidance frame formulation
  Vehicle’s engine is not vectored
  Control system is perfect with zero lag
  Nozzle exit velocity is a known constant
  Thrust magnitude upper bound is known
  State can be reliably measured at all times, including local gravitational acceleration
  Thrust is throttleable between minimum and maximum values
  Upon ignition, the throttle response is instantaneous

## Slide 7: Literature Review

## Slide 8: Apollo Powered Descent Guidance
APDG developed by Cherry 1964 and studied extensively by many.
Studies include programming methods, landing site redesignation (Ploen, Sostaric), robustness (Klumpp), and fuel performance comparisons performed by many.
Fuel performance is not optimal, as demonstrated by D’Souza, Najson, Ross, Lu, and many others.
APDG has been flown in real Apollo missions

## Slide 9: Adaptive Powered Descent Initiation
APDG and other powered descent guidance methods rely upon time-to-go estimates, which are often not optimized. D’Souza considered optimizing the time-to-go with a weighted function and realized a better fuel performance, but not completely optimal and did not address ignition timing. Others have explored similar avenues but have used predetermined ignition strategies.
Cerimele et al, designers of the CobraMRV, recommend a strategy similar to the one presented here but do not explore it.
Meditch showed in 1964 that fuel optimal thrust was “bang-bang” style for 1D descent. Leitmann 1959 showed the same for 2D using multiple switches, and Lu has shown that the same is true of 3D.

## Slide 10: Methodology

## Slide 11: APDG Derivation
Cherry derived E-Guidance and APDG, a version of E-Guidance, by framing powered descent as separate boundary value problems in each dimension. Vector boundary conditions in position and velocity for E-Guidance, and final attitude through thrust acceleration for APDG, form the constraints of the problem.
Final attitude control helps ensure soft landing under practical mission conditions
Choosing the command removes the non-linearities of the gravitational acceleration
Satisfying two final constraints given arbitrary initial condition requires two basis functions for the command. The addition of final attitude constraint requires a third basis function. Cherry chose , and for simplicity.
E-Guidance:
APDG:

## Slide 12: E-Guidance and APDG Implementation
E-Guidance
APDG
The E matrix, the inverted matrix forming the linear system from the equations of motion, gives E-Guidance its name. Each axis of motion is solved independently, resulting in a total of 6 at each guidance update
APDG forms a similar linear system in 3 unknowns per axis, resulting in the above 3 equations for a total of 9 at each guidance update.

## Slide 13: E-Guidance as Optimal Control
E-Guidance is not fuel optimal, but is the solution to an optimal control problem with a different performance index
The index does penalize large thrust magnitudes and the solution has been shown to give good performance
Applying optimal control theory (maximizing the Hamiltonian H) results in a command of the same form as E-Guidance
APDG may not minimize the same cost function but is shown to provide similar fuel performance
Fuel Optimal:
E-Guidance

## Slide 14: Time-to-go
The E-matrix for APDG relies upon a time-to-go estimate which is not addressed by the optimal control solution. The Apollo missions used an iterative method which had to allow for manual landing site redesignation and relied upon pre-mission planning. Many estimation methods could suffice, but since the focus of this thesis is the Adaptive PDI strategy the method used is based on performance and safety.
Citron, Dunin, and Meissinger developed the gravity turn guidance solution, wherein the thrust vector is always opposite the velocity and velocity is zeroed upon landing. This solution cannot ensure landing at a particular site, but its time-to-go might be considered a minimum for a given mission. A safety margin of can added for vacuum conditions, but atmospheric conditions prove not to need adjustment even with specification of landing site.

## Slide 15: Adaptive Powered Descent Initiation
Few powered descent guidance formulations consider optimized engine ignition time, though most acknowledge the need for ignition criteria. These are typically predetermined altitudes, groundranges, etc
Adaptive PDI uses the gravity turn solution as a threshold value. When required thrust exceeds maximum available thrust, or when groundrange traveled by a gravity turn exceeds ground distance to the landing site, the engine is ignited.
These criteria are shown to be robust

## Slide 16: Simulation
Architecture and Implementation

## Slide 17: Simulation Architecture
Monte-Carlo: Disperse Conditions
Record run data
Simulation
Guidance Computer
Navigation Module
Numerical Integration
Landed?
End
Aerodynamic Model
Yes
No
Runs completed?
Yes
No

## Slide 18: Aerodynamic Model
CobraMRV provided by Cerimele et al
  “rigid, enclosed, elongated lifting body shape that provides a higher lift-to-drag ratio (L/D) than a typical entry capsule”
  Designed for atmospheric entry and powered descent on Mars. Missions require 20 tonnes of cargo to the surface.
  Vehicle mass at PDI is 58000 kg. Max thrust is 800 kN, and min is 200 kN.
  and are empirical functions of Mach number and AoA. Reference area .
  Upon ignition, drag and lift are reduced by half due to effects of the exhaust plume.
  Optimal AoA is , which is held until ignition for Adaptive PDI.
Atmosphere model is NASA Mars GRAM

## Slide 19: Monte Carlo Testing
Dispersion applied to initial conditions, navigation measurements, rocket parameters (initial mass, thrust bounds, exhaust velocity)
Each run is seeded for reproducibility

## Slide 20: Initial Conditions
Initial trajectory modeled as small angle miss over landing site with overshoot.
Adaptive PDI is compared to predetermined conditions representing CobraMRV gliding at optimal AoA unpowered along initial trajectory. Cases 1-6 represent the predetermined conditions
Case 7 represents a spacecraft at condition 6 employing Adaptive PDI (initially unpowered)
6
5
4
3
2
1
7

## Slide 21: Results and Discussion
APDG is compared to E-Guidance. Adaptive PDI is examined vs. predetermined ignition times, with consideration of performance and safety.

## Slide 22: Adaptive PDI Criteria
Vacuum
Atmosphere

## Slide 23: E-Guidance vs. APDG
Thrust
Pitch
Fuel Performance
E-Guidance and APDG show opposite thrust profiles but similar fuel performance
APDG does drive pitch angle close to zero upon landing, while E-Guidance lands pitched up at

## Slide 24: Vacuum vs. Atmosphere
Thrust Magnitude
Vehicle Mass

## Slide 25: Vacuum Performance of Adaptive PDI

## Slide 26: Vacuum Performance: Nominal Results
Speed
Altitude

## Slide 27: Vacuum Performance: Nominal Results
Ground Range
Thrust

## Slide 28: Vacuum Performance: Dispersed Results
Case 1 Failures
Fuel Performance
Adaptive PDI (Case 7) shows middling fuel performance in Vacuum compared to predetermined cases.
But Case 1 shows good mean fuel performance but also results in landing failures (clear by the high final speeds). Case 1 fails 45/1000 landings.

## Slide 29: Adaptive PDI in Vacuum
Mediocre fuel performance
Guaranteed safety
  Vacuum requires for safety margin
Predetermined cases demonstrate that aggressive start (closer to landing site) gives better fuel performance at the cost of safety

## Slide 30: Atmospheric Performance of Adaptive PDI

## Slide 31: Atmospheric Performance: Nominal Results
Speed
Altitude

## Slide 32: Atmospheric Performance: Nominal Results
Ground Range
Thrust

## Slide 33: Atmospheric Performance: Dispersed Results
Case 1 Failures
Fuel Performance
Adaptive PDI (Case 7) shows excellent fuel performance in Vacuum compared to predetermined cases
Case 1 shows slightly worse mean fuel performance than other cases and also results in landing failures. Case 1 fails 13/1000 landings.

## Slide 34: Adaptive PDI in Atmosphere
Excellent fuel performance
Guaranteed safety
  Atmosphere does not require factor applied to
Predetermined cases perform similarly regardless of range to landing site, but Case 1 fails making choice critical. PDI alleviates this uncertainty and gives the best fuel performance due to two factors
  Time spent with engine off
  Aerodynamic effects at optimal AoA during unpowered glide

## Slide 35: Future Work

## Slide 36: Adaptive PDI: Applicability
Adaptive PDI is well suited to missions with high fuel inefficiency penalty and safety criticality. Future research should address other mission contexts, ex. other bodies or Earth landings
Any mission involving multiple burn phases could benefit from Adaptive PDI strategy. Other guidance algorithms should be tested in combination with Adaptive PDI

## Slide 37: Adaptive PDI: Generalization
Two variables for implementation of Adaptive PDI depend upon proper mission planning
  The time-to-go factor applied in vacuum, , but not applied in atmosphere is mission dependent. Ideally this would be some function of dynamic pressure or other local atmospheric measurement. Further work is necessary.
  The threshold values for the PDI criteria are taken directly from the gravity turn solution, and . There is some flexibility here in that some fraction of these values could be used to drive different performance. The exact relationship between these thresholds and the time-to-go factor should be explored