## Slide 1: An Evaluation of Apollo Powered Descent Guidance
Lloyd David Stroll III

## Slide 2: Statement of Purpose

## Slide 3: Powered Descent Guidance
Powered descent phase required for any mission in low or no atmosphere
Apollo Powered Descent Guidance (APDG) flown in vacuum only
Simple implementation makes APDG an easy testbed for Adaptive Powered Descent Initiation strategy

## Slide 4: Adaptive Powered Descent Initiation
Most powered descent strategies rely upon time-to-go estimate
Predetermined ignition point is open-loop. Closed-loop strategy might provide better performance and safety
Adaptive PDI helps improve safety and performance automatically

## Slide 5: Manned Mars Mission
Manned Mars missions are the focus of current efforts in aerospace, including NASA, SpaceX, and others
Manned Mars missions have high payload mass and large propellant inefficiency penalty
Safety criticality for landing
Vehicle studied is CobraMRV (Cerimele et al)

## Slide 6: Literature Review

## Slide 7: Apollo Powered Descent Guidance
APDG developed by Cherry 1964 and studied extensively by many.
Studies include programming methods, landing site redesignation (Ploen, Sostaric), robustness (Klumpp), and fuel performance comparisons performed by many.
Fuel performance is not optimal, as demonstrated by D’Souza, Najson, Ross, Lu, and many others.
APDG has been flown in real Apollo missions

## Slide 8: Adaptive Powered Descent Initiation
APDG and other powered descent guidance methods rely upon time-to-go estimates, which are often not optimized. D’Souza considered optimizing the time-to-go with a weighted function and realized a better fuel performance, but not completely optimal and did not address ignition timing. Others have explored similar avenues but have used predetermined ignition strategies.
Ceremele et al, designers of the CobraMRV, recommend a strategy similar to the one presented here but do not explore it.
Meditch showed in 1964 that fuel optimal thrust was “bang-bang” style for 1D descent. Leitmann 1959 showed the same for 2D using multiple switches, and Lu has shown that the same is true of 3D.

## Slide 9: Methodology

## Slide 11: Results and Discussion

## Slide 12: Future Work